Debian 3.1 ZoneMinder Server

Install Manual

By Koenzie

Table of Contents

Introduction	3

Hardware	4

Step 1. Installing Debian 3.1 Base	5

Step 2. Installing ZoneMinder	7

Step 3. Setting up ZoneMinder	10

Step 4. Adding a Monitor	11

Step 5. Configuring motion detection	12

# Introduction

This manual guides you trough the installation of a Debian 3.1 r0a server installation running the ZoneMinder video camera security and surveillance solution.

All steps are listed and the installation can be preformed with little Linux knowledge.

The setup time for a complete ZoneMinder system is less then one our.

# Hardware

The hardware used for this project :

  - Servercase

  - Intel Mainboard

  - Pentium IV processor

  - 512mb memory

  - Maxtor boot disc

Maxtor storage disc

# Step 1.	Installing Debian 3.1 Base

Download the Debian 3.1 r0a iso at http://www.debian.org

(Make sure you get the 1cd version)

Burn the Debian iso file on a 700mb cd-r

Boot your system using the cd you just burned

Select English

Select other

Select Netherlands

Select American English

Insert a unique hostname

Insert a domain name

Select Manually edit partition table

Select Guided partitioning

Select Erase entire disk: IDE1 master...

Select All files in one partition

Select IDE2

Select Create new partition

Change mount point to /video

Return to main menu

It looks something like this now :

Partitions :	Disk 1		EXT3			/

SWAP			SWAP

Disk 2		EXT3			/video

Select Finish partitioning and write changes to disk

Select Yes

Wait until the GRUB boot laoder message comes up and select Yes

Select Continue

Let the system reboot

Select Ok on the Welcome message

Select No on the Time zone configuration message

Select Yes, your Time zone is Europe/Amsterdam

Set root password, and verify it

Set user fullname

Set user shortname

Set user password, and verify it

Select ftp for the Apt configuration

Mirror country : Netherlands

Debian mirror : download.xs4all.nl

Select no other Debian software, just select Ok

Select local delivery only; not on a network

Select Ok

Select Ok

Login on your system

Your Debian server system is ready for use now!

Follow the next chapter to install ZoneMinder and all the dependencies

# Step 2.	Installing ZoneMinder

Login using your root account

Type vi /etc/apt/sources.list

Add the following lines (press ESC and i to insert) :

deb ftp://ftp.nerim.net/debian-marillat/ experimental main

deb ftp://ftp.nerim.net/debian-marillat/ sarge main

deb http://www.spic.net/zoneminder/debian/ ./

deb-src http://www.spic.net/zoneminder/debian/ ./

Copy the XS4ALL deb line and change stable into sarge (press ESC and x to delete)

(press ESC and yy to copy, ESC and o to add an new line and ESC p to past)

Copy the XS4ALL line again and change stable into etch

Press ESC and : and type wq to save and exit vi

Type apt-get update

Type apt-get dist-upgrade to upgrade the kernel

Press y to continue every time a question is asked

Set all the other options depending on your own wishes

Type apt-get install apache2

Press y to continue every time a question is asked

Type apt-get install php5

Press y to continue every time a question is asked

Type apt-get install php5-mysql

Press y to continue every time a question is asked

Type apt-get install libapache2-mod-auth-mysql

Press y to continue every time a question is asked

Type /etc/init.d/apache2 restart

Type apt-get install ntpdate

This installs a time update program

Type ntpdate time.tue.nl

This updates the time from time.tue.nl

Type apt-get install zm

Press y to continue every time a question is asked

Type vi /var/www/testphp.php

Add the following line (press ESC and i to insert) :

<?php phpinfo(); ?>

Press ESC and : and type wq to save and exit vi

Test apache and php with another pc by going to the following adress :

http://yourip/testphp.php

Type vi /var/www/zm/zm.php

Find setcookie by pressing ESC and typing :?setcookie

Create a new line under the setcookie statement by pressing ESC and o

Add the following line under setcookie (press ESC and i to insert) :

setcookie (“cookies”,$cookies);

Press ESC and : and type wq to save and exit vi

Type vi /etc/sysctl.conf

Add the following line (press ESC and i to insert) :

kernel.shmmax = 134217728

Press Esc and : and type wq to save and exit vi

Type vi /etc/apache2/sites-available/default

Change the following line (press ESC and i to insert) :

RedirectMatch ^/$ /apache2-default/

Into

RedirectMatch ^/$ /zm/

This will make zm the default apache startup directory

Press ESC and : and type wq to save and exit vi

Type mkdir /video/events

Type chown www-data /video/events

Type mkdir /video/images

Type chown www-data /video/images

Type ln -s var/www/video ./video

Type chown www-data video

Type ln -s /video/event ./events

Type ln -s /video/images ./images

Type chown www-data events

Type chown www-data images

Type vi /etc/network/interfaces

Change the following line (press ESC and i to insert text) :

iface eth0 inet dhcp

Into

iface et0 inet static

address “your assigned IP address”

netmask “your assigned netmask”

gateway “your assigned gateway”

This will set your static IP address

Press ESC and : and type wq to save and exit vi

Type reboot

This will restart the server and reload all services

# Step 3.	Setting up ZoneMinder

Use a other pc to preform the following steps

Open your webbrowser and surf to http://yourip

Login using the following information :

Username : admin

Password : admin

Click options on the right upperside of the window

A popup appears (be sure you turned of your popup blocker)

Click config

Uncheck timestamp images

Press save

Click web

Rename title zm to Signet

Uncheck console window resize

Press save

Click video

Check jpeg instead of mpeg

Press save

Click users

Click admin

Change password

Press save

Click add new user

Set username Signet

Set password

Set stream view

Set event view

Set monitors view

Set system view

Press save

Close the options window

# Step 4.	Adding a Monitor

Click add monitor

A popup appears (be sure you turned of your popup blocker)

Change Name (choose a name that represents the location)

Change Function to Modect to monitor and record

Change source type to remote to use a IP camera

Press save

Click source

Change remote host name use this mask :

user:password@IP

Change remote path, for a axis camera use :

/axis-cgi/mjpg/video.cgi

Change capture width : 640

Change capture height : 480

Change orientation if the cam is upside down, you can also do this on the IP cam

Press save

Close the monitor window

The monitor you just added appears in the console window.

You can test the monitor by clicking on the monitors name.

A window appears where you can see the camera's image and the events recorded.

Here you can also view events and delete them.

# Step 5.	Configuring motion detection